## Slide 1
Chapter 2 Application Layer
Computer Networking: A Top Down Approach, 5th edition. Jim Kurose, Keith Ross Addison-Wesley, April 2009.
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) in substantially unaltered form, that you mention their source (after all, we’d like people to use our book!)
If you post any slides in substantially unaltered form on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2009
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 Socket programming with UDP
2.8 Socket programming with TCP

## Slide 4: Chapter 2: Application Layer
Our goals:
conceptual, implementation aspects of network application protocols
  transport-layer service models
  client-server paradigm
  peer-to-peer paradigm
learn about protocols by examining popular application-level protocols
  HTTP
  FTP
  SMTP / POP3 / IMAP
  DNS
programming network applications
  socket API

## Slide 5: Some network apps
e-mail
web
instant messaging
remote login
P2P file sharing
multi-user network games
streaming stored video clips
social networks
voice over IP
real-time video conferencing
grid computing

## Slide 6: Creating a network app
write programs that
  run on (different) end systems
  communicate over network
  e.g., web server software communicates with browser software
No need to write software for network-core devices
  Network-core devices do not run user applications
  applications on end systems allows for rapid app development, propagation
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 7: Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 Socket programming with UDP
2.8 Socket programming with TCP

## Slide 8: Application architectures（题）
Client-server
  Including data centers / cloud computing
Peer-to-peer (P2P)
Hybrid of client-server and P2P
Notes: 应用架构 VS 网络架构
边缘 接入 核心

## Slide 9: Client-server architecture
server:
  always-on host
  permanent IP address
  server farms for scaling
clients:
  communicate with server
  may be intermittently connected
  may have dynamic IP addresses
  do not communicate directly with each other
client/server
Notes: 用于扩展的服务器群

## Slide 10: Google Data Centers
20 data centers, two are located in Asia
Google spent $16B since 2007 on new data centers
Each data center uses 50-100 megawatts of power
Notes: 百万瓦特
https://www.51cto.com/article/550929.html

## Slide 11: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
peers are intermittently connected and change IP addresses
Highly scalable but difficult to manage
peer-peer

## Slide 12: Hybrid of client-server and P2P
Skype
  voice-over-IP P2P application
  centralized server: finding address of remote party:
  client-client connection: direct (not through server)
Instant messaging (QQ)
  chatting between two users is P2P
  centralized service: client presence detection/location
    user registers its IP address with central server when it comes online
    user contacts central server to find IP addresses of buddies

## Slide 13: Processes communicating
Process: program running within a host.
within same host, two processes communicate using inter-process communication (defined by OS).
processes in different hosts communicate by exchanging messages
Client process: process that initiates communication
Server process: process that waits to be contacted
Note: applications with P2P architectures have client processes & server processes
Notes: 举一个过去蓝屏的例子

## Slide 14: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure, on other side of door which brings message to socket at receiving process
process
TCP with
buffers,
variables
socket
host or
server
process
TCP with
buffers,
variables
socket
host or
server
Internet
controlled
by OS
controlled by
app developer
API: (1) choice of transport protocol; (2) ability to fix a few parameters (lots more on this later)

## Slide 15: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Exercise: use ipconfig from command prompt to get your IP address (Windows)
Q: does IP address of host on which process runs suffice for identifying the process?

## Slide 16: Addressing processes
  A: No, many processes can be running on the same host
Identifier includes both IP address and port numbers associated with process on host.
Example port numbers:
  HTTP server: 80
  Mail server: 25
Use netstat –ano to get the port usage.

## Slide 17: App-layer protocol defines
Types of messages exchanged,
  e.g., request, response
Message syntax:
  what fields in messages & how fields are delineated
Message semantics
  meaning of information in fields
Rules for when and how processes send & respond to messages
（题）Public-domain protocols:
defined in RFCs
allows for interoperability
e.g., HTTP, SMTP, BitTorrent
Proprietary protocols:
e.g., Skype, ppstream
GET /somedir/page.html HTTP/1.1
Host: www.someschool.edu
User-agent: Mozilla/4.0
Connection: close
Accept-language:fr

## Slide 18: What transport service does an app need?
Data loss
some apps (e.g., audio) can tolerate some loss
other apps (e.g., file transfer, telnet) require 100% reliable data transfer
Timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
Throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
Security
Encryption, data integrity, …

## Slide 19: Transport service requirements of common apps
Application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video
interactive games
instant messaging
Data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
Throughput
elastic
elastic
elastic
audio: 5kbps-1Mbps
video:10kbps-5Mbps
same as above
few kbps up
elastic
Time Sensitive
no
no
no
yes, 100’s msec
yes, few secs
yes, 100’s msec
yes and no

## Slide 20: Internet transport protocols services
TCP service:
connection-oriented: setup required between client and server processes
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum throughput guarantees, security
UDP service:
unreliable data transfer between sending and receiving process
does not provide: connection setup, reliability, flow control, congestion control, timing, throughput guarantee, or security
Q: why bother? Why is there a UDP?
Notes: 航空信 挂号信

## Slide 21: Internet apps: application, transport protocols
Application
e-mail
remote terminal access
Web
file transfer
streaming multimedia
Internet telephony
Application
layer protocol
SMTP [RFC 2821]
Telnet [RFC 854]
HTTP [RFC 2616]
FTP [RFC 959]
HTTP (eg Youtube), RTP [RFC 1889]
SIP, RTP, proprietary
(e.g., Skype)
Underlying
transport protocol
TCP
TCP
TCP
TCP
TCP or UDP
typically UDP

## Slide 22: Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 Socket programming with UDP
2.8 Socket programming with TCP

## Slide 23: Web and HTTP
First some jargon
Web page consists of objects
Object can be HTML file, JPEG image, Java applet, audio file,…
Web page consists of base HTML-file which includes several referenced objects
Each object is addressable by a URL
Example URL:
www.someschool.edu/someDept/pic.gif
host name
path name
Notes: 学校的快递货架
host name: 小南门
path name: 2号货架，第3层，第5格

## Slide 24: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, “displays” Web objects
  server: Web server sends objects in response to requests
PC running
Explorer
Server
running
Apache Web
server
Mac running
Navigator
HTTP request
HTTP request
HTTP response
HTTP response

## Slide 25: HTTP overview (continued)
Uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
Protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 26: HTTP connections
Nonpersistent HTTP
At most one object is sent over a TCP connection.
Persistent HTTP
Multiple objects can be sent over single TCP connection between client and server.

## Slide 27: Non-Persistent HTTP: Response time
Definition of RTT: time for a small packet to travel from client to server and back.
Response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time
total = 2RTT+transmit time
time to
transmit
file
initiate TCP
connection
RTT
request
file
RTT
file
received
time
time
Notes: -听得到吗？(线路)
-听得到
-我想咨询个问题/发起个投诉。（业务）
-请讲

## Slide 28: Nonpersistent HTTP
Suppose user enters URL www.someSchool.edu/someDepartment/home.index
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(contains text,
references to 10
jpeg images)

## Slide 29: Nonpersistent HTTP (cont.)
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time

## Slide 30: Persistent HTTP
Nonpersistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open parallel TCP connections to fetch referenced objects
Persistent HTTP
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects

## Slide 31: HTTP request message（题）
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
GET /somedir/page.html HTTP/1.1
Host: www.someschool.edu
User-agent: Mozilla/4.0
Connection: close
Accept-language:fr
(extra carriage return, line feed)
request line
(GET, POST,
HEAD commands)
header
lines
Carriage return（回车）,
line feed （换行）
indicates end
of message

## Slide 32: HTTP request message: general format

## Slide 33: Uploading form input
Post method:
Web page often includes form input
Input is uploaded to server in entity body
URL method:
Uses GET method
Input is uploaded in URL field of request line:
www.somesite.com/animalsearch?monkeys&banana

## Slide 34: Method types
HTTP/1.0
GET
POST
HEAD
  asks server to leave requested object out of response
HTTP/1.1
GET, POST, HEAD
PUT
  uploads file in entity body to path specified in URL field
DELETE
  deletes file specified in the URL field
Notes: HTTP版本不断迭代
GET和POST的数据量越来越失衡，HTTP的POST需要传视频和音频
HTTP的版本迭代也在优化这个问题

## Slide 35: HTTP response message（题）
HTTP/1.1 200 OK
Connection close
Date: Thu, 06 Aug 1998 12:00:15 GMT
Server: Apache/1.3.0 (Unix)
Last-Modified: Mon, 22 Jun 1998 …...
Content-Length: 6821
Content-Type: text/html
data data data data data ...
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
HTML file

## Slide 36: HTTP response status codes
200 OK
  request succeeded, requested object later in this message
301 Moved Permanently
  requested object moved, new location specified later in this message (Location:)
400 Bad Request
  request message not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
In first line in server->client response message.
A few sample codes:

## Slide 37: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
Opens TCP connection to port 80
(default HTTP server port) at cis.poly.edu.
Anything typed in sent
to port 80 at cis.poly.edu
telnet cis.poly.edu 80
2. Type in a GET HTTP request:
GET /~ross/ HTTP/1.1
Host: cis.poly.edu
By typing this in (hit carriage
return twice), you send
this minimal (but complete)
GET request to HTTP server
3. Look at response message sent by HTTP server!

## Slide 39: User-server state: cookies
Many major Web sites use cookies
Four components:
  1) cookie header line of HTTP response message
  2) cookie header line in HTTP request message
  3) cookie file kept on user’s host, managed by user’s browser
  4) back-end database at Web site
Example:
Susan always access Internet always from PC
visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
  unique ID
  entry in backend database for ID

## Slide 40: Cookies: keeping “state” (cont.)
client
server
usual http response msg
usual http response msg
cookie file
one week later:
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual http request msg
Amazon server
creates ID
1678 for user
create
entry
usual http response
Set-cookie: 1678
ebay 8734
amazon 1678
usual http request msg
cookie: 1678
cookie-
spectific
action
access
ebay 8734
amazon 1678
backend
database

## Slide 41: Cookies (continued)
What cookies can bring:
authorization
shopping carts
recommendations
user session state (Web e-mail)
Cookies and privacy:
cookies permit sites to learn a lot about you
you may supply name and e-mail to sites
aside
How to keep “state”:
protocol endpoints: maintain state at sender/receiver over multiple transactions
cookies: http messages carry state

## Slide 42: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
  object in cache: cache returns object
  else cache requests object from origin server, then returns object to client
Goal: satisfy client request without involving origin server
client
Proxy
server
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
origin
server
HTTP response
HTTP response
Notes: https://worktile.com/kb/ask/1942272.html
爱奇艺的服务器

## Slide 43: More about Web caching
cache acts as both client and server
typically cache is installed by ISP (university, company, residential ISP)
Why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link.
Internet dense with caches: enables “poor” content providers to effectively deliver content (but so does P2P file sharing)

## Slide 44: Caching example（题）
Assumptions
average object size = 1,000,000 bits
avg. request rate from institution’s browsers to origin servers = 15/sec
delay from the Internet side router to any origin server and back to router = 2 sec
Consequences
utilization on LAN = 15%
utilization on access link = 100%
total delay = Internet delay + access delay + LAN delay
= 2 sec + minutes + milliseconds
origin
servers
public
Internet
institutional
network
100 Mbps LAN
15 Mbps
access link
institutional
cache
Notes: 为什么是minutes？因为是假设到达率提高到大于1的情况下，Internet delay不变，LAN delay不变，但是access delay指数级增长

## Slide 45: Caching example (cont)
possible solution
increase bandwidth of access link to, say, 100 Mbps
consequence
utilization on LAN = 15%
utilization on access link = 15%
Total delay = Internet delay + access delay + LAN delay
= 2 sec + msecs + msecs
often a costly upgrade
origin
servers
public
Internet
institutional
network
100 Mbps LAN
100 Mbps
access link
institutional
cache
Notes: 全部时延=request从host到institutional router（1/n LAN时延）+institutional router到接入router（1/m access delay）+接入router到目的server，数据从目的server返回到接入路由（Internet Delay）+内容从接入路由到institutional router（1-1/m access delay）+ 数据从从institutional router到host（1-1/n LAN时延）

## Slide 46: Caching example (cont)
possible solution: install cache
suppose hit rate is 0.4
consequence
40% requests will be satisfied almost immediately
60% requests satisfied by origin server
utilization of access link reduced to 60%, resulting in negligible delays (say 10 msec)
total avg delay = Internet delay + access delay + LAN delay = .6*(2.01) secs + .4*milliseconds < 1.4 secs
origin
servers
public
Internet
institutional
network
100 Mbps LAN
15 Mbps
access link
institutional
cache
Notes: 2.01=2s（Internet Delay)+0.01s（Access Delay），占到60%
LAN delay是毫秒级的，占到40%

## Slide 47: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
cache: specify date of cached copy in HTTP request
  If-modified-since: <date>
server: response contains no object if cached copy is up-to-date:
  HTTP/1.0 304 Not Modified
cache
server
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object
not
modified
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0 200 OK
<data>
object
modified

## Slide 48: Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 Socket programming with UDP
2.8 Socket programming with TCP

## Slide 49: FTP: the file transfer protocol
transfer file to/from remote host
client/server model
  client: side that initiates transfer (either to/from remote)
  server: remote host
ftp: RFC 959
ftp server: port 21
file transfer
FTP
server
FTP
user
interface
FTP
client
local file
system
remote file
system
user
at host
Notes: 像图书馆

## Slide 50: FTP: separate control, data connections
FTP client contacts FTP server at port 21, TCP is transport protocol
client authorized over control connection
client browses remote directory by sending commands over control connection.
when server receives file transfer command, server opens 2nd TCP connection (for file) to client
after transferring one file, server closes data connection.
FTP
client
FTP
server
TCP control connection
port 21
TCP data connection
port 20
server opens another TCP data connection to transfer another file.
control connection: “out of band”
FTP server maintains “state”: current directory, earlier authentication
Notes: 端口号Port和进程Process，类似于食堂打饭，端口号是窗口好，进程是食堂工作人员。Control是下单，Data是取餐

## Slide 51: FTP commands, responses
Sample commands:
sent as ASCII text over control channel
USER username
PASS password
LIST return list of file in current directory
RETR filename retrieves (gets) file
STOR filename stores (puts) file onto remote host
Sample return codes
status code and phrase (as in HTTP)
331 Username OK, password required
125 data connection already open; transfer starting
425 Can’t open data connection
452 Error writing file

## Slide 52: Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 Socket programming with UDP
2.8 Socket programming with TCP

## Slide 53: Electronic Mail
Three major components:
user agents
mail servers
simple mail transfer protocol: SMTP
User Agent
a.k.a. “mail reader”
composing, editing, reading mail messages
e.g., Eudora, Outlook, elm, Mozilla Thunderbird
outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
SMTP
SMTP
SMTP

## Slide 54: Electronic Mail: mail servers
Mail Servers
mailbox contains incoming messages for user
message queue of outgoing (to be sent) mail messages
SMTP protocol between mail servers to send email messages
  client: sending mail server
  “server”: receiving mail server
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
SMTP
SMTP
SMTP

## Slide 55: Electronic Mail: SMTP [RFC 2821]
uses TCP to reliably transfer email message from client to server, port 25
direct transfer: sending server to receiving server
three phases of transfer
  handshaking (greeting)
  transfer of messages
  closure
command/response interaction
  commands: ASCII text
  response: status code and phrase
messages must be in 7-bit ASCII

## Slide 56: Scenario: Alice sends message to Bob
1) Alice uses UA to compose message and “to” bob@someschool.edu
2) Alice’s UA sends message to her mail server; message placed in message queue
3) Client side of SMTP opens TCP connection with Bob’s mail server
4) SMTP client sends Alice’s message over the TCP connection
5) Bob’s mail server places the message in Bob’s mailbox
6) Bob invokes his user agent to read message
user
agent
mail
server
mail
server
user
agent
1
2
3
4
5
6

## Slide 57: Sample SMTP interaction
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok
C: RCPT TO: <bob@hamburger.edu>
S: 250 bob@hamburger.edu ... Recipient ok
C: DATA
S: 354 Enter mail, end with "." on a line by itself
C: Do you like ketchup?
C: How about pickles?
C: .
S: 250 Message accepted for delivery
C: QUIT
S: 221 hamburger.edu closing connection

## Slide 58: Try SMTP interaction for yourself:
telnet servername 25
see 220 reply from server
enter HELO, MAIL FROM, RCPT TO, DATA, QUIT commands
above lets you send email without using email client (reader)
telnet smtp.bupt.edu.cn 25

## Slide 59: 题

## Slide 60
Notes: 注意有的是Received by，有的是Received from

## Slide 61: SMTP: final words
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
Comparison with HTTP:
HTTP: pull
SMTP: push
both have ASCII command/response interaction, status codes
HTTP: each object encapsulated in its own response msg
SMTP: multiple objects sent in multipart msg

## Slide 62: Mail message format
SMTP: protocol for exchanging email msgs
RFC 822: standard for text message format:
header lines, e.g.,
  To:
  From:
  Subject:
  different from SMTP commands!
body
  the “message”, ASCII characters only
header
body
blank
line

## Slide 63: Mail access protocols
SMTP: delivery/storage to receiver’s server
Mail access protocol: retrieval from server
  POP: Post Office Protocol [RFC 1939]
    authorization (agent <-->server) and download
  IMAP: Internet Mail Access Protocol [RFC 1730]
    more features (more complex)
    manipulation of stored msgs on server
  HTTP: gmail, Hotmail, Yahoo! Mail, etc.
user
agent
sender’s mail
server
user
agent
SMTP
SMTP
access
protocol
receiver’s mail
server

## Slide 64: POP3 protocol
authorization phase
client commands:
  user: declare username
  pass: password
server responses
  +OK
  -ERR
transaction phase, client:
list: list message numbers
retr: retrieve message by number
dele: delete
quit
C: list
S: 1 498
S: 2 912
S: .
C: retr 1
S: <message 1 contents>
S: .
C: dele 1
C: retr 2
S: <message 1 contents>
S: .
C: dele 2
C: quit
S: +OK POP3 server signing off
S: +OK POP3 server ready
C: user bob
S: +OK
C: pass hungry
S: +OK user successfully logged on

## Slide 65: POP3 (more) and IMAP
More about POP3
Previous example uses “download and delete” mode.
Bob cannot re-read e-mail if he changes client
“Download-and-keep”: copies of messages on different clients
POP3 is stateless across sessions
IMAP
Keep all messages in one place: the server
Allows user to organize messages in folders
IMAP keeps user state across sessions:
  names of folders and mappings between message IDs and folder name

## Slide 66: Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 Socket programming with UDP
2.8 Socket programming with TCP

## Slide 67: DNS: Domain Name System
People: many identifiers:
  SSN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., ww.yahoo.com - used by humans
Q: map between IP addresses and name ?
Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol host, routers, name servers to communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 68: DNS
Why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
doesn’t scale!
DNS services
hostname to IP address translation
host aliasing
  Canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: set of IP addresses for one canonical name
Notes: 中心化的DNS没法扩容

## Slide 69: Distributed, Hierarchical Database
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
poly.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
Client wants IP for www.amazon.com; 1st approx:
client queries a root server to find com DNS server
client queries com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com
Notes: apporx 举例 类似与12345 市长热线

## Slide 70: DNS: Root name servers
contacted by local name server that can not resolve name
root name server:
  contacts authoritative name server if name mapping not known
  gets mapping
  returns mapping to local name server
13 root name servers worldwide
b USC-ISI Marina del Rey, CA
l ICANN Los Angeles, CA
e NASA Mt View, CA
f Internet Software C. Palo Alto, CA (and 36 other locations)
i Autonomica, Stockholm (plus 28 other locations)
k RIPE London (also 16 other locations)
m WIDE Tokyo (also Seoul, Paris, SF)
a Verisign, Dulles, VA
c Cogent, Herndon, VA (also LA)
d U Maryland College Park, MD
g US DoD Vienna, VA
h ARL Aberdeen, MD
j Verisign, ( 21 locations)
Notes: 实际上，DNS 根服务器的数量远不止13个。13个字母只是一个符号性的表示方式，用于方便标识这些根服务器的名称。每个字母代表一个名为“根区域”的逻辑区域，而每个根区域都由多个实际的根服务器组成，以提供冗余和高可用性。
每个根区域都有多个根服务器，它们被称为“根服务器实例”或“根服务器镜像”。这些实例分布在全球各地的多个地理位置和数据中心，由不同的组织和运营商负责。这样做是为了确保 DNS 服务的稳定性、可靠性和快速响应。

## Slide 71: TLD and Authoritative Servers
Top-level domain (TLD) servers:
  responsible for com, org, net, edu, etc, and all top-level country domains uk, fr, ca, jp.
  Network Solutions maintains servers for com TLD
  Educause for edu TLD
Authoritative DNS servers:
  organization’s DNS servers, providing authoritative hostname to IP mappings for organization’s servers (e.g., Web, mail).
  can be maintained by organization or service provider
Notes: Root, TLD, Auth.
三层，每层有自己的工作
Root 储存了不同的TLD（比如 行业.com 和 国家）
TLD储存了不同的Auth（不同组织，比如说baidu.com)
Auth储存了baidu.com的IP地址

## Slide 72: Local Name Server
does not strictly belong to hierarchy
each ISP (residential ISP, company, university) has one.
  also called “default name server”
when host makes DNS query, query is sent to its local DNS server
  acts as proxy, forwards query into hierarchy

## Slide 73: DNS name resolution example
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu
iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”
Notes: 循环，雷锋问路（把困难留给自己），常用

## Slide 74: DNS name resolution example
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
3
recursive query:
puts burden of name resolution on contacted name server
heavy load?
Notes: 递归，找雷锋问路（雷锋把困难留给自己），不常用

## Slide 75: DNS: caching and updating records（课后题）
once (any) name server learns mapping, it caches mapping
  cache entries timeout (disappear) after some time
  TLD servers typically cached in local name servers
    Thus root name servers not often visited
update/notify mechanisms under design by IETF
  RFC 2136
  http://www.ietf.org/html.charters/dnsind-charter.html

## Slide 76: DNS records
DNS: distributed db storing resource records (RR)
Type=NS
  name is domain (e.g. foo.com)
  value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
Type=A
  name is hostname
  value is IP address
Type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really
  servereast.backup2.ibm.com
  value is canonical name
Type=MX
  value is name of mailserver associated with name

## Slide 77: DNS protocol, messages
DNS protocol : query and reply messages, both with same message format
msg header
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply
  recursion desired
  recursion available
  reply is authoritative

## Slide 78: DNS protocol, messages
Name, type fields
for a query
RRs in response
to query
records for
authoritative servers
additional “helpful”
info that may be used

## Slide 79: Inserting records into DNS
example: new startup “Network Utopia”
register name networkutopia.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts two RRs into com TLD server:
  (networkutopia.com, dns1.networkutopia.com, NS)
  (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server Type A record for www.networkutopia.com; Type MX record for networkutopia.com
How do people get IP address of your Web site?

## Slide 80: Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 Socket programming with UDP
2.8 Socket programming with TCP

## Slide 81: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
peers are intermittently connected and change IP addresses
Three topics:
  File distribution
  Searching for information
  Case Study: Skype
peer-peer

## Slide 82: File Distribution: Server-Client vs P2P
Question : How much time to distribute file from one server to N peers?
us
u2
d1
d2
u1
uN
dN
Server
Network (with
abundant bandwidth)
File, size F
us: server upload bandwidth
ui: peer i upload bandwidth
di: peer i download bandwidth

## Slide 83: File distribution time: server-client（课后题）
us
u2
d1
d2
u1
uN
dN
Server
Network (with
abundant bandwidth)
F
server sequentially sends N copies:
  NF/us time
client i takes F/di time to download
increases linearly in N
(for large N)
= dcs = max { NF/us, F/min(di) }
i
Time to distribute F
to N clients using
client/server approach

## Slide 84: File distribution time: P2P（课后题）
us
u2
d1
d2
u1
uN
dN
Server
Network (with
abundant bandwidth)
F
server must send one copy: F/us time
client i takes F/di time to download
NF bits must be downloaded (aggregate)
fastest possible upload rate: us + Sui
dP2P = max { F/us, F/min(di) , NF/(us + Sui) }
i
Notes: 因为N个Peers（除了服务器）都要下载Fbits，所以一共要下载NFbits，因此就要求所有客户端（包括服务器）必须上传NFbits，上传NFbits最快需要多少时间呢？是NF/(us + Sui)，是因为所有链路同时参与上传时是最快的。
最后的时间，是三个最小时间取了最大值。为什么？因为如果取最小值，所有文件没有完成上传/下载，等于说最后的任务没完成，就结束计时了。

## Slide 85
Server-client vs. P2P: example
Client upload rate = u, F/u = 1 hour, us = 10u, dmin ≥ us
Notes: N在增加 Sigma(u_i)也在增加，因为连加是从1加到N，所以不是线性的

## Slide 86: File distribution: BitTorrent
tracker: tracks peers
participating in torrent
torrent: group of
peers exchanging
chunks of a file
obtain list
of peers
trading
chunks
peer
P2P file distribution

## Slide 87: BitTorrent (1)
file divided into 256KB chunks.
peer joining torrent:
  has no chunks, but will accumulate them over time
  registers with tracker to get list of peers, connects to subset of peers (“neighbors”)
while downloading, peer uploads chunks to other peers.
peers may come and go
once peer has entire file, it may (selfishly) leave or (altruistically) remain

## Slide 88: BitTorrent (2)
Pulling Chunks
at any given time, different peers have different subsets of file chunks
periodically, a peer (Alice) asks each neighbor for list of chunks that they have.
Alice sends requests for her missing chunks
  rarest first
Sending Chunks: tit-for-tat
Alice sends chunks to four neighbors currently sending her chunks at the highest rate
  re-evaluate top 4 every 10 secs
every 30 secs: randomly select another peer, starts sending chunks
  newly chosen peer may join top 4
  “optimistically unchoke”

## Slide 89: BitTorrent: Tit-for-tat
(1) Alice “optimistically unchokes” Bob
(2) Alice becomes one of Bob’s top-four providers; Bob reciprocates
(3) Bob becomes one of Alice’s top-four providers
With higher upload rate, can find better trading
partners & get file faster!

## Slide 90: Distributed Hash Table (DHT)
DHT = distributed P2P database
Database has (key, value) pairs;
  key: ss number; value: human name
  key: content type; value: IP address
Peers query DB with key
  DB returns values that match the key
Peers can also insert (key, value) peers

## Slide 91: DHT Identifiers
Assign integer identifier to each peer in range [0,2n-1].
  Each identifier can be represented by n bits.
Require each key to be an integer in same range.
To get integer keys, hash original key.
  eg, key = h(“Led Zeppelin IV”)
  This is why they call it a distributed “hash” table

## Slide 92: How to assign keys to peers?
Central issue:
  Assigning (key, value) pairs to peers.
Rule: assign key to the peer that has the closest ID.
Convention in lecture: closest is the immediate successor of the key.
Ex: n=4; peers: 1,3,4,5,8,10,12,14;
  key = 13, then successor peer = 14
  key = 15, then successor peer = 1

## Slide 93: Circular DHT (1)
1
3
4
5
8
10
12
15
Each peer only aware of immediate successor and predecessor.
“Overlay network”

## Slide 94: Circle DHT (2)
0001
0011
0100
0101
1000
1010
1100
1111
Who’s resp
for key 1110 ?
I am
O(N) messages
on avg to resolve
query, when there
are N peers
1110
1110
1110
1110
1110
1110
Define closest as closest successor

## Slide 95: Circular DHT with Shortcuts
Each peer keeps track of IP addresses of predecessor, successor, short cuts.
Reduced from 6 to 2 messages.
Possible to design shortcuts so O(log N) neighbors, O(log N) messages in query
1
3
4
5
8
10
12
15
Who’s resp
for key 1110?

## Slide 96: Peer Churn
Peer 5 abruptly leaves
Peer 4 detects; makes 8 its immediate successor; asks 8 who its immediate successor is; makes 8’s immediate successor its second successor.
What if peer 13 wants to join?
1
3
4
5
8
10
12
15
To handle peer churn, require
each peer to know the IP address
of its two successors.
Each peer periodically pings its two successors to see if they are still alive.

## Slide 97: P2P Case study: Skype（题）
inherently P2P: pairs of users communicate.
proprietary application-layer protocol (inferred via reverse engineering)
hierarchical overlay with SNs
Index maps usernames to IP addresses; distributed over SNs
Skype clients (SC)
Supernode
(SN)
Skype
login server
Notes: overlay 覆盖 supernode 盖住 clients

## Slide 98: Peers as relays
Problem when both Alice and Bob are behind “NATs”.
  NAT prevents an outside peer from initiating a call to insider peer
Solution:
  Using Alice’s and Bob’s SNs, Relay is chosen
  Each peer initiates session with relay.
  Peers can now communicate through NATs via relay
Notes: relay 中继
SN 超级节点

## Slide 99: Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 Socket programming with UDP
2.8 Socket programming with TCP

## Slide 100: Socket programming
Socket API
introduced in BSD4.1 UNIX, 1981
explicitly created, used, released by apps
client/server paradigm
two types of transport service via socket API:
  UDP
  TCP
A application-created,
OS-controlled interface (a “door”) into which
application process can both send and
receive messages to/from another application process
socket
Goal: learn how to build client/server application that communicate using sockets

## Slide 101: Socket programming basics
Server must be running before client can send anything to it.
Server must have a socket (door) through which it receives and sends segments
Similarly client needs a socket
Socket is locally identified with a port number
  Analogous to the apt # in a building
Client needs to know server IP address and socket port number.

## Slide 102: Socket programming with UDP
UDP: no “connection” between client and server
no handshaking
sender explicitly attaches IP address and port of destination to each segment
OS attaches IP address and port of sending socket to each segment
Server can extract IP address, port of sender from received segment
application viewpoint
UDP provides unreliable transfer
of groups of bytes (“datagrams”)
between client and server
Note: the official terminology
for a UDP packet is “datagram”. In this class, we instead use “UDP segment”.

## Slide 103: Running example
Client:
  User types line of text
  Client program sends line to server
Server:
  Server receives line of text
  Capitalizes all the letters
  Sends modified line to client
Client:
  Receives line of text
  Displays

## Slide 104: Client/server socket interaction: UDP
Server (running on hostid)
close
clientSocket
read datagram from
clientSocket
create socket,
clientSocket =
DatagramSocket()
Client
Create datagram with server IP and
port=x; send datagram via clientSocket
create socket,
port= x.
serverSocket =
DatagramSocket()
read datagram from
serverSocket
write reply to
serverSocket
specifying client address,
port number

## Slide 105: Example: Java client (UDP)
Output: sends packet
Input: receives packet
Client
process
client UDP socket

## Slide 106: Example: Java client (UDP)
import java.io.*;
import java.net.*;
class UDPClient {
public static void main(String args[]) throws Exception
{
BufferedReader inFromUser =
new BufferedReader(new InputStreamReader(System.in));
DatagramSocket clientSocket = new DatagramSocket();
InetAddress IPAddress = InetAddress.getByName("hostname");
byte[] sendData = new byte[1024];
byte[] receiveData = new byte[1024];
String sentence = inFromUser.readLine();
sendData = sentence.getBytes();
Create
input stream
Create
client socket
Translate
hostname to IP
address using DNS

## Slide 107: Example: Java client (UDP), cont.
DatagramPacket sendPacket =
new DatagramPacket(sendData, sendData.length, IPAddress, 9876);
clientSocket.send(sendPacket);
DatagramPacket receivePacket =
new DatagramPacket(receiveData, receiveData.length);
clientSocket.receive(receivePacket);
String modifiedSentence =
new String(receivePacket.getData());
System.out.println("FROM SERVER:" + modifiedSentence);
clientSocket.close();
}
}
Create datagram with data-to-send,
length, IP addr, port
Send datagram
to server
Read datagram
from server

## Slide 108: Example: Java server (UDP)
import java.io.*;
import java.net.*;
class UDPServer {
public static void main(String args[]) throws Exception
{
DatagramSocket serverSocket = new DatagramSocket(9876);
byte[] receiveData = new byte[1024];
byte[] sendData = new byte[1024];
while(true)
{
DatagramPacket receivePacket =
new DatagramPacket(receiveData, receiveData.length);
serverSocket.receive(receivePacket);
Create
datagram socket
at port 9876
Create space for
received datagram
Receive
datagram

## Slide 109: Example: Java server (UDP), cont
String sentence = new String(receivePacket.getData());
InetAddress IPAddress = receivePacket.getAddress();
int port = receivePacket.getPort();
String capitalizedSentence = sentence.toUpperCase();
sendData = capitalizedSentence.getBytes();
DatagramPacket sendPacket =
new DatagramPacket(sendData, sendData.length, IPAddress,
port);
serverSocket.send(sendPacket);
}
}
}
Get IP addr
port #, of
sender
Write out
datagram
to socket
End of while loop,
loop back and wait for
another datagram
Create datagram
to send to client

## Slide 110: UDP observations & questions
Both client server use DatagramSocket
Dest IP and port are explicitly attached to segment.
What would happen if change both clientSocket and serverSocket to “mySocket”?
Can the client send a segment to server without knowing the server’s IP address and/or port number?
Can multiple clients use the server?

## Slide 111: Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  SMTP, POP3, IMAP
2.5 DNS
2.6 P2P applications
2.7 Socket programming with UDP
2.8 Socket programming with TCP

## Slide 112: Socket-programming using TCP
TCP service: reliable transfer of bytes from one process to another
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
internet

## Slide 113: Socket programming with TCP
Client must contact server
server process must first be running
server must have created socket (door) that welcomes client’s contact
Client contacts server by:
creating client-local TCP socket
specifying IP address, port number of server process
When client creates socket: client TCP establishes connection to server TCP
When contacted by client, server TCP creates new socket for server process to communicate with client
  allows server to talk with multiple clients
  source port numbers used to distinguish clients (more in Chap 3)
TCP provides reliable, in-order
transfer of bytes (“pipe”)
between client and server
application viewpoint

## Slide 114: Client/server socket interaction: TCP
wait for incoming
connection request
connectionSocket =
welcomeSocket.accept()
create socket,
port=x, for
incoming request:
welcomeSocket =
ServerSocket()
create socket,
connect to hostid, port=x
clientSocket =
Socket()
close
connectionSocket
read reply from
clientSocket
close
clientSocket
Server (running on hostid)
Client
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup

## Slide 115
Client
process
client TCP socket
Stream jargon
A stream is a sequence of characters that flow into or out of a process.
An input stream is attached to some input source for the process, e.g., keyboard or socket.
An output stream is attached to an output source, e.g., monitor or socket.

## Slide 116: Socket programming with TCP
Example client-server app:
1) client reads line from standard input (inFromUser stream) , sends to server via socket (outToServer stream)
2) server reads line from socket
3) server converts line to uppercase, sends back to client
4) client reads, prints modified line from socket (inFromServer stream)

## Slide 117: Example: Java client (TCP)
import java.io.*;
import java.net.*;
class TCPClient {
public static void main(String argv[]) throws Exception
{
String sentence;
String modifiedSentence;
BufferedReader inFromUser =
new BufferedReader(new InputStreamReader(System.in));
Socket clientSocket = new Socket("hostname", 6789);
DataOutputStream outToServer =
new DataOutputStream(clientSocket.getOutputStream());
Create
input stream
Create
client socket,
connect to server
Create
output stream
attached to socket

## Slide 118: Example: Java client (TCP), cont.
BufferedReader inFromServer =
new BufferedReader(new
InputStreamReader(clientSocket.getInputStream()));
sentence = inFromUser.readLine();
outToServer.writeBytes(sentence + '\n');
modifiedSentence = inFromServer.readLine();
System.out.println("FROM SERVER: " + modifiedSentence);
clientSocket.close();
}
}
Create
input stream
attached to socket
Send line
to server
Read line
from server

## Slide 119: Example: Java server (TCP)
import java.io.*;
import java.net.*;
class TCPServer {
public static void main(String argv[]) throws Exception
{
String clientSentence;
String capitalizedSentence;
ServerSocket welcomeSocket = new ServerSocket(6789);
while(true) {
Socket connectionSocket = welcomeSocket.accept();
BufferedReader inFromClient =
new BufferedReader(new
InputStreamReader(connectionSocket.getInputStream()));
Create
welcoming socket
at port 6789
Wait, on welcoming
socket for contact
by client
Create input
stream, attached
to socket

## Slide 120: Example: Java server (TCP), cont
DataOutputStream outToClient =
new DataOutputStream(connectionSocket.getOutputStream());
clientSentence = inFromClient.readLine();
capitalizedSentence = clientSentence.toUpperCase() + '\n';
outToClient.writeBytes(capitalizedSentence);
}
}
}
Read in line
from socket
Create output
stream, attached
to socket
Write out line
to socket
End of while loop,
loop back and wait for
another client connection

## Slide 121: TCP observations & questions
Server has two types of sockets:
  ServerSocket and Socket
When client knocks on serverSocket’s “door,” server creates connectionSocket and completes TCP conx.
Dest IP and port are not explicitly attached to segment.
Can multiple clients use the server?

## Slide 122: Chapter 2: Summary
application architectures
  client-server
  P2P
  hybrid
application service requirements:
  reliability, bandwidth, delay
Internet transport service model
  connection-oriented, reliable: TCP
  unreliable, datagrams: UDP
our study of network apps now complete!
specific protocols:
  HTTP
  FTP
  SMTP, POP, IMAP
  DNS
  P2P: BitTorrent, Skype
socket programming

## Slide 123: Chapter 2: Summary
typical request/reply message exchange:
  client requests info or service
  server responds with data, status code
message formats:
  headers: fields giving info about data
  data: info being communicated
Most importantly: learned about protocols
Important themes:
control vs. data msgs
  in-band, out-of-band
centralized vs. decentralized
stateless vs. stateful
reliable vs. unreliable msg transfer
“complexity at network edge”